Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model: 	     		Indoor/Outdoor

- 82% Efficiency

- ASME Code Glass-Lined Cast Iron Headers

- ASME Code Copper Fin Tube

- 125 lb. Pressure Relief Valve

- Small Footprint

- Unitherm Governor Anti-Condensation Control

- Internal Bypass for High Flow Rates (up to 125 gpm)

- Indoor/Outdoor

#### Heat Exchanger

ASME Inspected and Stamped
160 PSIG

National Board Approved

Glass-lined Cast Iron Headers

Finned Tubing

Copper – Standard

Cupro Nickel – Optional

ASME Steel Tube Sheet

Silicone O-Rings

125 PSIG Pressure Relief Valve

Water Connections

Right Hand – Standard

Left Hand – Field Change

Flow Configuration – Two-pass

#### Controls – Millivolt Option

Standing Pilot Ignition

Thermopile Generator

Single Mechanical Sensor

Flame Rollout Switch

High Limit Control

On/Off Switch

Water Pressure Switch

#### Controls – Digital Option

115/230V, 60Hz, 1 Ph Power Supply

115/230/24V Transformer

100% Pilot Shut-off; Lockout – Propane units only

Electronic, Intermittent Ignition Pilot (IID)

High Limit Control

On/Off Switch

Flame Rollout Switch

Water Pressure Switch

Dual Electronic Temp Sensor

Digital Display With Diagnostics

#### Gas Control Train

Fuel

Natural Gas

Propane

Combination Control Valve

On/Off Firing

ANSI Z21.56 Design Certified

#### Construction

Front Controls

Stainless Steel Burners

Polytuf Powder Coat Finish

Indoor/Outdoor

Vent Selection

Outdoor Stackless Top – Standard

Indoor Draft Diverter– Loose

D-2 Power Vent – Loose

Base (Optional)

Combustible Floor Shield

RP2100 – ASME Series

Atmospheric Pool Heaters	Model

# Text boxes

# RP2100™

# ASME Series

# Atmospheric Pool Heaters

# Models 185B-405B

Digital model with outdoor top shown

NOTES:

Model number suffix indicates pilot type (E = digital, M = millivolt) and fuel type (P = propane, N = natural gas). Prefix “C” indicates Cast Iron (ASME) headers. Example: Model number CR-405B-EN indicates an ASME unit with digital (IID) ignition using natural gas.

Ratings are for natural gas and elevations up to 2,000 feet above sea level. Reduce input 4% for each 1,000 feet above sea level when installed at over 2,000 feet elevation.

Manufactured under Patent  No. 3,623,458.

| Heater Model | BTUH Input (000) | (A) Cabinet Width | (B) Flue Dia. | (C) Indoor Drafthood | (J) | Gas Conn. | Water Conn. | Shipping Weights (lbs) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Heater with Stackless Top | Indoor Drafthood |
| R185B | 181 | 18-1/4” | 6” | 62-5/8” | 12-1/16” | 3/4" | 2” | 191 | 12 |
| R265B | 264 | 22-3/8” | 7” | 62-7/8” | 11-1/8” | 3/4" | 2” | 214 | 15 |
| R335B | 334 | 25-3/4” | 8” | 63-3/4” | 10-3/4” | 3/4" | 2” | 234 | 17 |
| R405B | 399 | 29-1/4” | 9” | 65-3/8” | 12-1/2” | 3/4" | 2” | 253 | 20 |

Raypak, Inc. ( 2151 Eastman Avenue, Oxnard, CA  93030 ( (805) 278-5300 ( Fax (800) 872-9725 (  www.raypak.com

Raypak Canada Ltd. ( 2805 Slough St., Mississauga, Ontario, Canada L4T 1G2 ( (905) 677-7999 ( Fax (905) 677-8036 ( www.raypakcanada.com