Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model:  	     		Indoor/Outdoor:        	 	MBTUH Input:

Sealed Combustion Chamber

100% Factory Fire Tested

Efficiency: 85%

Minimum Non-condensing Inlet Temperature: 105°F

Thermal Shock Proof Heat Exchanger

Limited Twenty-year Thermal Shock Warranty

Limited Five-year Heat Exchanger Warranty

Full Safety Diagnostics with Fault History

PolyTuf Powder Coated Cabinet

No Combustible Floor Shield Required

Fan-assisted

Non-ferrous Bypass

Patented Burner Security Blanket

Heat Exchanger

Brass Headers

ASME Inspected and Stamped
160 PSIG Working Pressure

National Board Approved

Cupro-Nickel Finned Tubing

ASME Steel Tube Sheet

Silicone High-Temp O-Rings

125 PSIG ASME Pressure Relief Valve

Temperature and Pressure Gauge

Water Connections

Left – Standard

Right – Option A-6

Bronze Pump, 1/2 HP, 120V, 60Hz

Non-ferrous Pool Bypass

Controls

120V, 60Hz, 1( Power Supply

120/24V 60Hz Transformer

100% Shut-off/Lockout

Hot Surface Ignition System

Remote Flame Sensor

High Limit Control, Auto Reset

On/Off Power Switch

Manual Shut-off, Front-mounted

Flow Switch

Blocked Vent Pressure Switch

Combustion Air Proving Switches

Economaster Pump Time Delay

Poolstat

Diagnostics Panel with LCD Panel

2 Lines, 20 Characters

Gas Train

Combination Valves

On/Off Firing

Low Gas Pressure Switch, Manual

Fuel

Natural Gas

Propane Gas

Design Certified ANSI Z21.56/
CSA 4.7

Burner

Ultra-low NOx:
Less than 20 PPM

Construction

Indoor/Outdoor Construction

Enclosed Front Controls

CSA Low Lead Certified ≤ .25% Lead

Venting

Vent Location

Top – Standard

Rear – Option D-14

Vent Termination Cap

Outdoor – Option D-11

Indoor, Horizontal – 
Option D-15

Indoor, Vertical (by others)

Combustion Air

In-Line Filter Kit (TruSeal only) – Option D-17

Air Intake Elbow – 
Option D-16

Multi-Heater Controllers

B-26	2-Stage Digital

B-21	4-Stage Digital

B-__	TempTracker Mod+ (Up to 16 Boilers)

B-60	Stage Interface

Options

C-6	Ignition Module, Manual Reset

D-21	TruSeal® Direct Vent

Left Side - Standard 
 Right Side - Optional

F-10		Low Water Cut-off, Remote Probe

P-__	Cold Water Run System

(See Page 3 Sizes 992B-1262B only)

S-2	High Gas Pressure Switch, Manual (Dual switches on Model 1532B)

X-1	SureRack® Kit (Lower Unit Requires Manifold Modification)

X-2	SureRack® Kit, Above Grade

Add-on (Used with X-1) (Lower Unit Requires Manifold Modification)

Regulatory Agency Requirements

G-1	CSD-1

Hi Delta – Type P

Models 992B-1262B (H-Bypass)		        				Model

Hi Delta – Type P

Models 992B-1262B (Cold Water Run Bypass)				Model

| Model | MBTUH | A Width | K | W | Amp Draw (w/ Pump) | Pump HP | Injector Pump HP | Shipping Weight (Lbs.) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Input | Output |  |  |  |  |  |  |  |
| P 992B | 990 | 842 | 57-1/8 | 10 | 16-13/16 | < 16 | 1/2 | 1/3 * | 1000 |
| P 1262B | 1260 | 1071 | 68-1/2 | 12 | 20-9/16 | < 16 | 1/2 | 1/3 * | 1055 |

# Text boxes

# Hi Delta® - Type P

## Commercial Pool Heaters Models 992B-1262B

Patent No. 7,044,124

Standard “H” Bypass Shown

Proudly Assembled in the USA

For Metric information, see Catalog

Standard “H” Bypass

RATE OF FLOW AND PRESSURE DROP

| Model | Max. Flow |
| --- | --- |
|  | GPM | ∆P (ft) | ∆T |
| 992B | 132 | 14.0 | 13 |
| 1262B | 132 | 15.5 | 16 |

| Model | MBTUH | A | K | W | Amp Draw (w/ Pump) | Shipping Weight (Lbs.) |
| --- | --- | --- | --- | --- | --- | --- |
|  | Input | Output | Width |  |  |  |  |
| 992B | 990 | 842 | 57-1/8 | 10 | 16-13/16 | < 16 | 900 |
| 1262B | 1260 | 1071 | 68-1/2 | 12 | 20-9/16 | < 16 | 1010 |

Dimensions are in inches.

Ratings shown are for elevations up to 4,500 feet and for natural or propane gas.

For installation at elevations over 4,500 feet, please contact manufacturer.

* Separate 120 VAC or 240 VAC 1Ø power required for Cold Water Run option.

Injector pump shipped loose for field installation at bypass inlet.

Dimensions are in inches.

Ratings shown are for elevations up to 4,500 feet and for natural or propane gas.

For installations at elevations over 4,500 feet, please contact manufacturer.

RATE OF FLOW AND PRESSURE DROP

| Model | Max. Flow |
| --- | --- |
|  | GPM | ∆P (ft) | ∆T |
| 992B | 132 | 14.0 | 13 |
| 1262B | 132 | 15.5 | 16 |

Raypak, Inc. ▪ 2151 Eastman Avenue, Oxnard, CA 93030 ▪ (805) 278-5300 ▪ Fax (805) 872-9725 ▪ www.raypak.com