Job:

Engineer:

Contractor:

Prepared By: 	     		 Date:

Indoor/Outdoor:

EFFICIENT

82% thermal efficiency – highest of any atmospheric water heater available today

THERMAL SHOCK PROOF

Twenty-year warranty against thermal shock damage
up to 150°F differential

Maximum operating temperature: 210°F

LIGHTWEIGHT

A floor load of 70 lbs./sq. ft. or less

HIGH RECOVERY

Cuts fuel costs substantially because the standby and 
radiation losses associated with tank-type water heaters
are eliminated

LOW WATER OPERATING TEMPERATURE

Operates with water temperature as low as
105°F without condensing

#### Heat Exchanger

ASME Inspected and Stamped
160 PSIG

National Board Approved

Bronze Headers

Copper Fin Tubing

ASME Steel Tube Sheet

Silicone O-Rings

125 PSIG ASME Pressure Relief Valve

Temperature and Pressure Gauge,
Shipped Loose

Four-pass Heat Exchanger

Pump – Optional

Mounted, 1/8 HP, 120 VAC, 1 60 Hz

#### Controls

120V, 60Hz, 1 Ph Power Supply

120/24V Transformer

100% Pilot Shut-off/Lockout

Electronic, Intermittent Ignition (IID) Pilot

High Limit Control, Auto Reset – 200°F

On/Off Switch

Flue Gas Spillage Switch

Economaster II Pump Time Delay

Flame Roll-out Sensor

#### Gas Control Train

Manual Main Gas Shut-off Cock

Main Gas Pressure Regulator

Redundant Safety Shut-off Valve

Control Valve

Firing Mode

On/Off (WH1)

Mechanical Modulation (WH2)

Fuel

Natural Gas

Propane Gas

Design Certified ANSI Z21.10.3

#### Construction

Front Controls

Stainless Steel Burners

PolyTuf Powder Coat Finish

Vent Selection

Drafthood (Indoor) – 
Option D-10

Stackless Top (Outdoor) – 
Option D-11

High-Wind Top (Outdoor) – 
Option D-13

Base – Optional

Combustible Floor Shield – 
Option J-1

CSA Low Lead Certified ≤ .25 Pb

Temperature Controls

B-2	Single-Stage Tankstat 
(100-180°F)

B-3	2-Stage Tankstat (100-180°F)

B-26	2-Stage Digital (Loose)

B-21	4-Stage Digital (Loose)

#### Additional Safety Controls

Raytherm – Type WH

Model 133

| Model No. | INDOOR | OUTDOOR | Approx. Shipping Weight (Lbs.) |
| --- | --- | --- | --- |
|  | Input MBTUH | Output MBTUH | Output MBTUH | Without Pump | With Pump |
| WH-133 | 136 | 112 | 109 | 160 | 186 |

NOTES:	Dimensions are in inches.

Ratings shown are for elevations up to 2,000 feet. For elevations over 2,000 feet, reduce ratings 4% for 
each 1,000 feet above sea level.

###### HEATER RATES OF FLOW AND PRESSURE DROPS

| 10((T | 20((T | 30((T | 40((T |
| --- | --- | --- | --- |
| GPM | (P (ft) | GPM | (P (ft) | GPM | (P (ft) | GPM | (P (ft) |
| 22 | 14.7 | 11 | 3.8 | N/A | N/A | N/A | N/A |

HEATER RECOVERY RATES (GPH)

|  | Temperature Rise |
| --- | --- |
|  | 20°F | 30°F | 40°F | 50°F | 60°F | 80°F | 100°F |
| INDOOR | 669 | 446 | 335 | 268 | 223 | 167 | 134 |
| OUTDOOR | 653 | 435 | 327 | 261 | 218 | 163 | 131 |

# Text boxes

# Raytherm® - Type WH

## Water Heaters
Commercial

Model 133

INDOOR MODEL ILLUSTRATED

Raypak, Inc.  (  2151 Eastman Avenue, Oxnard, CA  93030  (  (805) 278-5300  (  Fax (800) 872-9725  (  www.raypak.com