Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model: 	     		Indoor/Outdoor:

100% Factory Fire Tested

Efficiency: 84%

Maximum Outlet Temperature: 210°F

Minimum Non-Condensing Inlet Temperature: 105°F

Thermal Shock Proof Heat Exchanger

Footprint: Less Than 5-1/2 ft2

Limited Twenty-Year Thermal Shock Warranty

Limited Ten-Year Heat Exchanger Warranty

Ten-Year Unconditional Burner Head Warranty

Operation Status Center and Full Diagnostic Panel

#### Heat Exchanger

Bronze Headers

ASME Inspected and Stamped
160 PSIG Working Pressure

National Board Approved

Finned Cupro-Nickel Tubes

ASME Steel Tube Retainer

Silicone High Temp O-Rings

125 PSIG ASME Pressure Relief Valve

Temperature and Pressure Gauge, Shipped Loose

#### Control

120V, 60Hz, Power Supply

120/24V 60Hz Transformer

100% Pilot Shutoff/Lockout

Pilot: Electronic Intermittent Ignition (I.I.D.)

High Limit Control, Manual Reset

High Limit Control, Auto Reset

On/Off Switch

Flow Switch

Blocked Vent Pressure Switch

Combustion Air Proving Switch

Time Delay Pump Off Control

Central Point Wiring Diagnostics Panel

#### Burner

Aerodynamically Stabilized
Non-Clog  Burner

Ultra-Low NOx: Less than 30 PPM

#### Gas Train

Fuel

Natural Gas

Propane (Models 751 & 1001)

Manual Gas Shut-off Valves

Gas Pressure Regulator

Safety Shut-off Valve

Firing Control Valve

Low Gas Pressure Switch, Manual

On/Off Firing Mode

Design Certified ANSI Z21.10.3

#### Construction

Indoor/Outdoor Construction

Front Controls Enclosed

PolyTuf Powder Coat Finish

Connections (Water, Electrical, Gas)

Rear – Standard

Right Side – Option A-8

#### Venting

Vent Location

Rear – Standard

Right Side – Option Z-2

Vent Termination Cap

Outdoor – Option D-11

Indoor, Horizontal – Option D-15

Indoor, Vertical (by others)

#### Temperature Controls

B-2	Single-Stage Tankstat, 
100-180°F

B-3	2-Stage Tankstat, 100-180°F

B-21	4-Stage TempTracker 
Digital Controller

B-26	2-Stage TempTracker 
Digital Controller

Y-241	Electronic Sequencer, 
1-4 Stages

Y-281	Electronic Sequencer, 
5-8 Stages

#### Additional Safety Controls (Optional)

F-10	Low Water Cut-off, Remote Probe

S-2	Manual High Gas Pressure Switch

#### Regulatory Agency Requirements

C-5	Ignition Lockout Module

#### Other Equipment

Condensing Heat Exchanger

Pump

Soft Water (0-4 grains)

Medium Water (5-15 grains)

Hard Water (16+ grains)

ADB – Type WH

Models 751-1501	Model

| Model | MBTUH | B | D | E | F | G | H | K | M | P | Ship Weight | Foot-print | Amps* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Input | Output | Height |  |  |  | NPT | NPT | Flue ( |  |  | (Lbs.) | (Ft2) |  |
| WH 751 | 750 | 630 | 64 | 38 | 44-1/2 | 29-3/4 | 1-1/2 | 2 | 8 | 17-3/4 | 41 | 680 | 5.4 | 8 |
| WH 1001 | 999 | 840 | 72 | 46 | 52-1/2 | 37-3/4 | 1-1/2 | 2-1/2 | 10 | 21-1/2 | 49 | 720 | 5.4 | 10 |
| WH 1501 | 1499 | 1260 | 82 | 56 | 62-1/2 | 47-3/4 | 1-1/2 | 2-1/2 | 12 | 20-1/4 | 59 | 780 | 5.4 | 12 |

Dimensions are in inches

Ratings shown are for elevations up to 5,000 feet. For installations at elevations

over 5,000 feet, please consult the factory for instructions.

NOTE:  For direct vent applications, please contact the factory about relocating the pump.

| Model | RATES OF FLOW AND PRESSURE DROPS | RECOVERY RATES (GPH) |
| --- | --- | --- |
|  | 20ºF (T | 30ºF (T | 40ºF (T | Max. Flow | Min. Flow | Temperature Rise at 84% Efficiency |
|  | GPM | (P (ft) | GPM | (P (ft) | GPM | (P (ft) | GPM | (P (ft) | (T | GPM | (P (ft) | (T | 20°F | 30°F | 40°F | 50°F | 60°F | 80°F | 100°F |
| WH 751 | 63 | 5.8 | 42 | 2.9 | 32 | 1.8 | 110 | 17.0 | 11°F | 32 | 1.8 | 40°F | 3780 | 2520 | 1890 | 1512 | 1260 | 945 | 756 |
| WH 1001 | 84 | 11.8 | 56 | 5.6 | 42 | 3.4 | 110 | 20.0 | 15°F | 42 | 3.4 | 40°F | 5040 | 3360 | 2520 | 2016 | 1680 | 1260 | 1008 |
| WH 1501 | 126 | 31.4 | 84 | 14.9 | 63 | 9.1 | 126 | 31.4 | 20°F | 63 | 9.1 | 40°F | 7560 | 5040 | 3780 | 3024 | 2490 | 1890 | 1512 |

# Text boxes

# ADB™ - Type WH

## Water Heaters

Models 751-1501

* Current draw does NOT include pump.

(Supply breaker must have delayed trip.)

Raypak, Inc.  (  2151 Eastman Avenue, Oxnard, CA  93030  (  (805) 278-5300  (  Fax (800) 872-9725  (  www.raypak.com

Certified Clearances

Front	24” (for service)

Rear	12” (water side)

Right	1”

Left	1”

Top	0” (see note 1)

Floor	0” (see note 2)

Vent	1”

Notes:

1.	24” required for service

2.	DO NOT install on carpeting