Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model:  	     		Indoor/Outdoor:

EFFICIENT

82% thermal efficiency – highest of any atmospheric
boiler available today

THERMAL SHOCK PROOF

Twenty-year warranty against thermal shock damage
up to 150°F differential

Maximum operating temperature: 230°F

LIGHTWEIGHT

A floor load of 70 lbs./sq. ft. or less

HIGH RECOVERY

Cuts fuel costs substantially because the standby and
radiation losses normal to other boilers are eliminated

LOW WATER OPERATING TEMPERATURE

Operates with water temperature as low as 105°F
without condensing

#### Heat Exchanger

ASME Inspected and Stamped
160 PSIG

National Board Approved

Glass-lined Cast Iron Headers

Copper Finned Tubing

ASME Steel Tube Sheet

Silicone O-Rings

45 PSIG ASME Pressure Relief Valve

Temperature and Pressure Gauge, Shipped Loose

Rear Water Connection

Pump – Optional

Bronze, 1/8 HP, 120 Volt, 1 60 Hz

Cast Iron, 1/8 HP, 120 Volt, 1 
60 Hz

#### Controls

120V, 60Hz, 1 Ph Power Supply

120/24V Transformer

100% Pilot Shut-off/Lockout

Electronic, Intermittent Ignition (IID) Pilot

High Limit Control - Automatic

On/Off Switch

Operating Limit Control

Economaster II Pump Time Delay

#### Gas Train

Manual Main Gas Shut-off Cock

Main Gas Pressure Regulator

Redundant Safety Shut-off Valve

Control Valve

Mechanical Modulation (H1)

Fuel

Natural Gas

Propane Gas

Design Certified ANSI Z21.13/
CSA 4.9

#### Construction

Front Controls

Stainless Steel Burners

Polytuf Powder Coat Finish

Vent Selection

Draft Diverter (Indoor) – 
Option D-10

Stackless Top (Outdoor) – 
Option D-11

High-Wind Top (Outdoor) – 
Option D-13

Base – Optional

Combustible Floor Shield – 
Option J-1

Vent Damper – Indoor Residential models only

CSA Certified – AB 1953 & VLA 193 Low Lead Compliant

NOTE: Unit cannot be installed 
outdoors in residential applications.

Raytherm - Type H

Hydronic Heating Boilers		Model 133

| Model No. | Input MBTUH | Indoor | Outdoor | Power Requirements 120 VAC | Shipping Weight Lbs. (Approx.) |
| --- | --- | --- | --- | --- | --- |
|  |  | Output MBTUH | AFUE | Output MBTUH | With Pump | Without Pump |  |
| H-133 | 136 | 112 | 82.7% | 109 | < 10 Amps | < 1 Amp | 160 |

NOTES:

Ratings shown are for elevations up to 2,000 feet. For elevations over 2,000 feet, reduce
ratings at the rate of 4% for each 1,000 feet above sea level.

###### BOILER RATE OF FLOW AND PRESSURE DROP

| 10((T | 20((T | 30((T | 40((T |
| --- | --- | --- | --- |
| GPM | (P FT. | GPM | (P FT. | GPM | (P FT. | GPM | (P FT. |
| 22 | 14.7 | 11 | 3.8 | N/A | N/A | N/A | N/A |

# Text boxes

# Raytherm® - Type H

## Hydronic Heating Boilers
Residential ( Commercial

Model 133

Indoor Model

Proudly Made in the USA

Raypak, Inc.  (  2151 Eastman Avenue, Oxnard, CA  93030  (  (805) 278-5300  (  Fax (800) 872-9725  (  www.raypak.com