Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model: 	     		Indoor/Outdoor:

100% Factory Fire Tested

Efficiency: 84%

Maximum Outlet Temperature: 230°F

Minimum Non-condensing Inlet Temperature: 105°F

Thermal Shock Proof Heat Exchanger

Footprint: Less than 5 ft2

CSD-1 Gas Train

Limited Twenty-Year Thermal Shock Warranty

Limited Ten-Year Heat Exchanger Warranty

Ten-Year Unconditional Burner Head Warranty

Operation Status Center and Full Diagnostic Panel

#### Heat Exchanger

Bronze Headers

ASME Inspected and Stamped
160 PSIG Working Pressure

National Board Approved

Finned Copper Tubes

ASME Steel Tube Retainer

Silicone High Temp O-Rings

Pressure Relief Valve - ASME

60 PSIG – Standard

PSIG – Optional

Temperature and Pressure Gauge, Shipped Loose

#### Control

120V, 60Hz, Power Supply

120/24V  60Hz, Transformer

100% Pilot Shutoff/Lockout

Pilot: Electronic Intermittent Ignition (I.I.D.)

High Limit Control, Manual Reset

Operating Limit Control, Auto Reset

On/Off Switch

Flow Switch

Blocked Vent Pressure Switch

Combustion Air Proving Switch

Time Delay Pump Off Control

Central Point Wiring Diagnostics Panel

#### Burner

Aerodynamically Stabilized Non-clog Burner

Ultra-low NOx: Less than 30 PPM

#### Gas Train (CSD-1)

Fuel

Natural Gas

Propane

Manual Gas Shut-off Valves

Gas Pressure Regulator

Safety Shut-off Valve

Firing Control Valve

Manual Low Gas Pressure Switch

On/Off Firing Mode (H4)

Design Certified ANSI Z21.13/
CSA 4.9

#### Construction

Indoor/Outdoor Construction

Enclosed Front Controls

PolyTuf Powder Coat Finish

Connections (Water, Electrical, Gas)

Rear – Standard

Right Hand – Option A-8

#### Venting

Vent Location

Rear – Standard

Right Side – Option Z-2

Vent Termination Cap

Outdoor - Option D-11

Indoor, Horizontal – Option D-15

Indoor, Vertical (by others)

#### Temperature Controls

B-20	Single-Stage Controller, 
100-200°F

B-6	2-Stage Controller, 
100-200°F

B-21	4-Stage TempTracker 
Digital Controller

B-23	4-Stage TempTracker Digital Controller, Outdoor Reset

Y-241	Electronic Sequencer, 
1-4 Stages

Y-281	Electronic Sequencer, 
5-8 Stages

#### Additional Safety Controls (Optional)

F-10	Low Water Cut-off, 
Remote Probe

S-2	Manual High Gas Pressure Switch

#### Regulatory Agency Requirements

C-5	Ignition Lockout Module

#### Other Equipment

Condensing Heat Exchanger

Pump

ADB - Type H

#### Model 500

|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Ship | Foot- |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MODEL | MBTUH | B | D | E | F | G | H | K | M | N | P | R | T | Weight | print | Amps* |
|  | Input | Output | Height |  |  |  | NPT | NPT |  |  |  |  |  |  | Lbs. | Ft.2 |  |
| H 500 | 500 | 420 | 49 | 46 | 30 | 22-1/2 | 1 | 2 | 6 | 13-3/4 | 8-5/8 | 40 | 22-1/4 | 6 | 545 | 4-3/4 | 8 |

Dimensions are in inches.	*	Current draw NOT including pump.

Ratings shown for elevations up to 5,000 feet for natural or propane gas.			(Supply breaker must have a delayed trip)

#### For installation at elevations over 5,000 feet, please consult factory.

#### NOTE:  For direct vent applications, please contact factory about relocating the pump.

BOILER RATES OF FLOW AND PRESSURE DROPS

|  | 20°F (T | MAX. FLOW | MIN. FLOW |
| --- | --- | --- | --- |
| MODEL | GPM | (P (ft) | GPM | (P (ft) | (T | GPM | (P (ft) | (T |
| H 500 | 42 | 2.6 | 84 | 8.8 | 10°F | 30 | 1.6 | 28°F |

Recommended natural gas pressure is 7-10.5” w.c.

#### Recommended propane gas pressure is 11-13” w.c.

# Text boxes

# ADB™ - Type H

## Hydronic Heating Boiler
Model 500

Clearance Requirements

Front	24” (for service)

Rear	1”

Right	12” (water side)

Left	1”

Top	0

Floor	0” *

Vent	1”

*DO NOT install on carpeting

Raypak, Inc.  (  2151 Eastman Avenue, Oxnard, CA  93030  (  (805) 278-5300  (  Fax (800) 872-9725  (  www.raypak.com